Lot Acceptance Report – L10d

STMicroelectronics

Laser Transmitters

Internal Report

D.Bailleux,M.M.Obertino, R.Zuyeuski

Table of Contents

1	Lot Validation Programme	3

1.1	Lot Validation programme workflow	3

2	Technical validation	4

2.1	Compliance with technical requirements	4

2.2	Validation test results	6

2.2.1 Visual Inspection	6

2.2.2 LIV Characteristics	6

2.2.3 Dynamic Measurement	8

3	Conclusions	9

# Lot Validation Programme

This is an internal lot validation report for the Laser Transmitters (Laserpills) supplied by STMicroelectronics under the terms of CERN Contract F 451/EP/CMS.  We sampled randomly 53 lasers (13.25% of   total number of lasers of the batch) from lot L10d. The 400 devices of this lot were delivered by ST in two times: 384 on September 30th 2003 and 16 at the beginning of November 2003. The validation procedure consisted of evaluation tests described in “Laser Transmitter Quality Assurance Procedure” (Document ID: CMS-TK-QP-0002).

## Lot Validation programme workflow

The lot validation programme flow is shown in Figure 1.  The figure shows the tests to be carried out as described in the test procedure for laserpills (CMS-TK-QP-0002).   The test target specifications are extracted from the technical specification for delivered laserpills (CMS-TK-ES-0004).  All tests were carried out at room temperature.

Figure 1:  Lot Validation testing flow.

Table 1:  ST Serial Numbers of the 51 L10d devices and their correpsonding CMS Serial Numbers

| ST Serial # | CMS Serial # | ST Serial # | CMS Serial # |
| --- | --- | --- | --- |
| XE304D00 XE304D12 XE312D07 XE359C98 XE363C53 XE363C67 XE363C84 XE363C85 XE364C18 XE364C23 XE364C24 XE364C86 XE365C66 XE365C77 XE367C06 XE371C07 XE371C08 XE371C37 XE371C56 XE371C65 XE372C14 XE372C32 XE372C40 XE372C41 XE372C43 XE372C46 XE372C49 | 30201010032842 30201010032092 30201010032215 30201010034819 30201010034813 30201010029025 30201010029306 30201010029388 30201010035960 30201010035840 30201010035804 30201010029986 30201010032162 30201010029264 30201010033009 30201010035983 30201010033449 30201010027382 30201010033018 30201010033060 30201010032780 30201010029429 30201010032719 30201010027524 30201010029103 30201010032856 30201010029703 | XE372C59 XE372C71 XE372C74 XE372C95 XE372C99 XE373C19 XE373C71 XE373C94 XE373C96 XE374C05 XE374C23 XE375C13 XE375C23 XE375C25 XE375C36 XE375C37 XE375C40 XE375C41 XE375C60 XE375C73 XE392C51 XE392C60 XE392C68 XE392C82 XE392C84 XE392C87 | 30201010029535 30201010029111 30201010029671 30201010029913 30201010032882 30201010032011 30201010032333 30201010029882 30201010029740 30201010032079 30201010029364 30201010029119 30201010035875 30201010035882 30201010032278 30201010032445 30201010032423 30201010032404 30201010029732 30201010029781 30201010033937 30201010033410 30201010029352 30201010027919 30201010035887 30201010032723 |

# Technical validation

## Compliance with technical requirements

Table 2 shows the specified performance of the laser transmitters against which the received sample was tested.  The table also gives a summary of the results obtained in comparison with the specifications.

Table 2:  Specification test targets taken from the technical specification.  Cells in gray indicate parameters not measured during qualification.

| # | Specification to be tested | Test Target Specifications | CERN Validation Results |
| --- | --- | --- | --- |
|  |  | Min | Typ | Max | Units | Min | Max | Accepted? |
| 2.2.1 | Number of channels |  | 1 |  |  | 1 | 1 | Yes |
| 2.2.2 | Integral linearity deviation |  |  | 1 | % | 0.078 | 0.42 | Yes |
| 2.2.3 | Tensile load on connector side of pigtail |  |  | 7 | N |  |  |  |
| 2.2.4 | Tensile load on submount side of pigtail | 3 |  |  | N |  |  |  |
| 2.2.5 | Pigtail length Lp |  | 2 |  | m |  |  | Yes |
| 2.2.6 | Size |  |  | 4.5 ( 4 ( 1.35 | mm |  |  | Yes |
| 2.2.21 | Max. input current | 60 | 100 |  | mA | 60 |  | Yes |
| 2.2.22 | Threshold current |  | 5 | 10 | mA | 5.18 | 6.54 | Yes |
| 2.2.23 | Forward voltage |  | 1.2 | 1.75 | V | 1.499 | 1.826 | Yes |
| 2.2.24 | Reverse voltage | 2 |  |  | V |  |  |  |
| 2.2.25 | Rise time |  |  | 0.5 | ns | 0.197 | 0.275 | Yes |
| 2.2.41 | Wavelength | 1285 | 1310 | 1335 | nm |  |  |  |
| 2.2.42 | Fibre output power | 1.3 | 1.6 | 1.9 | mW | 1.381 | 1.938 | Yes |
| 2.2.43 | Slope efficiency | 0.032 | 0.04 | 0.048 | mW/mA | 0.035 | 0.049 | Yes |
| 2.2.44 | RIN |  | -130 |  | dB/Hz |  |  |  |
| 2.2.61 | Magnetic field |  |  | 4 | T |  |  |  |
| 2.2.62 | Hadronic fluence |  |  | 3×1014 | cm-2 |  |  |  |
| 2.2.63 | Gamma radiation dose |  |  | 1.5×105 | Gy(Si) |  |  |  |
| 2.2.64 | Temperature | -20 | -10 | 70 | °C |  |  |  |
| 2.2.65 | Operating humidity |  | Dry N2 flow |  |  |  |  |  |
| 2.2.81 | Optical safety |  | Laser Class 3A |  |  |  |  |  |
| 2.2.82 | Material composition |  | Halogen-free, flame retardant material |  |  |  |  |  |
| others | In-system test |  |  |  |  |  |  |  |

## Validation test results

### Visual Inspection

In two cases (30201010027524 and 30201010033009) the device was out of place in its shipping box glued to the sponges, therefore these two were taken out of the validation procedure. One laser (30201010029111) was rejected because of long scratch on the pad despite the following test did not show any problem its with performance. A long scratch was found on the fibre of 6 of the 51 lasers inspected (30201010029111, 30201010032333, 30201010032719, 30201010029264, 30201010035887 and 30201010035960) but we do not think this will create a problem for the performance of the fibre itself.

### LIV Characteristics

Figure 2, Figure 3 and Figure 4 show the results of the LIV measurements performed at CERN. The dashed lines indicate the range or maximum value allowed for each parameter. From the plots is clear that most of the lasers met the criteria given in the specifications.

Figure 2: CERN-measured threshold and efficiency for all 51 devices.

Figure 3: CERN-measured forward and fibre output power for all 51 devices.

Figure 4: Maximum value of the integral linearity deviation -measured at CERN for all 51 devices.

There are only two devices with parameters out of specifications: laser 30201010034813 with FV=1.837 V and laser 30201010034819 with Slope = 0.049 W/A and FOP = 1.938 W. Nevertheless, in order to take into account the difference between the two setups (at Cern and in Milano), it was established with ST to consider good the devices with parameters smaller than Max+5%, where Max is the maximum allowed value reported in table 2 . Taking into account this condition, all the lasers can be accepted.

Figure 5and Figure 6 show comparisons between CERN and ST measurements of Ith, Slope Efficiency and Forward Voltage.  The consistency between the two sets of measurements for the slope is good, but often the threshold is found bigger by CERN than by ST. Moreover, there is a large spread in the comparison of the forward voltage. Both this effects were already observed before (see Lot Acceptance Report L8 and L10A) and could be due to a difference in the measurements of the optical power and to the fact that the temperature in the CERN setup is not as stable as in the ST setup.

Figure 5: Comparison of CERN-measured Ith and eff iciency with the ST measurement In the histograms on the bottom the ST measurements are plotted in red, the CERN ones in black.

Figure 6: Comparison of CERN-measured Forward Voltage with the ST measurements. In the histograms on the bottom the ST measurements are plotted in red, the CERN ones in black.

### Dynamic Measurement

#### Rise Time

By applying a voltage pulse train to the laser under test it is possible to excite the laser to laser from below threshold.  By observing the resultant optical pulse on an oscilloscope with the aid of an optical probe one can measure the relaxation oscillations of the laser die and thus determine the intrinsic bandwidth of the die without the sub-mount.  A typical optical pulse is shown in Figure 7, while the extracted bandwidth and risetime are shown in Figure 8.

Figure 7 Optical output pulse measured on an oscilloscope using an optical probe.  The laser bandwidth is determined from the relaxation oscillation frequency.

Figure 8: Bandwidth and risetime for 51 devices that were measured at CERN was.   All devices are in spec: Bandwidth>1GHz.

# Conclusions

From 53 lasers taken randomly from batch L10d two devices were not validated due to packaging problem, and one was not accepted because of scratch, but all remaining lasers were found inside the criteria given in the specification. The lot is therefore accepted.

# Footnotes

Laser Transmitter Quality Assurance Procedure, Version 1.2, 17 January 2003

CMS Tracker Optical Readout Link Specification, Part 2.2: Laser Transmitter, Version 3.5, 14 May 2002