Lot Acceptance Report – L24a

STMicroelectronics

Laser Transmitters

Internal Report

R. Zuyeuski

Table of contents

1.	Lot Validation Program	3

2.	Technical validation	4

2.1	Compliance with technical requirements	4

2.2	Validation test results	4

2.2.1	Visual Inspection	4

2.2.2	LIV Characteristics	5

2.2.3	Dynamic Measurement	7

3.	Conclusions	8

# Lot Validation Program

This is an internal lot validation report for the Laser Transmitters (Laserpills) supplied by STMicroelectronics under the terms of CERN Contract F 451/EP/CMS. The lot validation testing flow is shown in Figure 1. The figure shows the tests to be carried out as described in the test procedure for laserpills (Laser Transmitter Quality Assurance Procedure; CMS-TK-QP-0002). The test target specifications are extracted from the technical specification for delivered laserpills (CMS-TK-ES-0004).

Figure 1.	Lot validation testing flow

40 lasers, or 5% of total number, of lot L24a delivered by ST in August 2004 were sampled randomly and tested (see Table 1). All tests were carried out at room temperature.

Table 1.	ST Serial Numbers of the 40 devices tested at CERN and their correpsonding CMS Serial Numbers

| ST Serial # | CMS Serial # | ST Serial # | CMS Serial # |
| --- | --- | --- | --- |
| 30201010000219 | XL418C18 | 30201010048525 | XL416C13 |
| 30201010000330 | XL435C29 | 30201010048530 | XL419C53 |
| 30201010000334 | XL435C31 | 30201010048564 | XL435C80 |
| 30201010000712 | XL416C96 | 30201010048582 | XL409C55 |
| 30201010000793 | XL418C64 | 30201010048588 | XL419C74 |
| 30201010001305 | XL419C11 | 30201010048589 | XL435C79 |
| 30201010001998 | XL419C23 | 30201010048717 | XL413C91 |
| 30201010004425 | XL415C90 | 30201010048722 | XL419C65 |
| 30201010004453 | XL417C89 | 30201010049115 | XL416C59 |
| 30201010048022 | XL416C70 | 30201010049128 | XL416C78 |
| 30201010048100 | XL435C72 | 30201010049290 | XL416C56 |
| 30201010048204 | XL410C77 | 30201010049326 | XL410C89 |
| 30201010048210 | XL410C16 | 30201010049330 | XL410C91 |
| 30201010048284 | XL418C76 | 30201010049358 | XL421C02 |
| 30201010048377 | XL420C06 | 30201010049396 | XL418C87 |
| 30201010048407 | XL417C01 | 30201010049555 | XL416C68 |
| 30201010048412 | XL416C61 | 30201010049558 | XL419C66 |
| 30201010048435 | XL421C93 | 30201010049604 | XL415C81 |
| 30201010048444 | XL417C02 | 30201010049936 | XL417C48 |
| 30201010048469 | XL419C75 | 30201010049987 | XL418C71 |

# Technical validation

## Compliance with technical requirements

Table 2 shows the specified performance of the laser transmitters against which the received sample was tested. The table also gives a summary of the results obtained in comparison with the specifications.

Table 2.	Specification test targets taken from the technical specification

| Specification to be tested | Test Target Specifications | CERN Validation Results |
| --- | --- | --- |
|  | Min | Max | Units | Min | Max |
| Threshold current |  | 10 | mA | 4.668 | 5.553 |
| Slope efficiency | 0.032 | 0.048 | mW/mA | 0.033 | 0.047 |
| Forward voltage |  | 1.75 | V | 1.533 | 1.643 |
| Fibre output power | 1.3 | 1.9 | mW | 1.271 | 1.815 |
| Integral linearity deviation |  | 1 | % | 0.190 | 0.318 |
| Rise time |  | 0.5 | ns | 1.219 | 2.110 |

## Validation test results

### Visual Inspection

All 800 devices from lot L24a have polyethylene-buffered fibre. 40 inspected lasers have no visible defects except for 2 cases: one laser (ST ID XL435C29) has relatively big spot of glue at the bottom side (see Figure 2a) that could create assembling problem; another one (ST ID XL410C77) has long scratches on pads (see Figure 2b). 40 more devices were inspected for the glue, and the same problem was observed for one laser (ST ID XL421C07). In all cases glue spots are close to the centre of laser.

Figure 2.	Laser contaminated with glue (a), and one with scratched pads (b).

In total, 3 devices out of 80 did not pass visual inspection.

### LIV Characteristics

Figure 3, Figure 4 and Figure 5 show the results of the LIV measurements performed at CERN. The colored lines indicate the range or maximum value allowed for each parameter. From the plots it is clear that almost all lasers met the criteria given in the specifications except for one device (ST ID XL419C23), with fiber output power below acceptable limit, but still within 5% tolerance.

Figure 3.	Efficiency and threshold for the 40 devices measured at CERN

Figure 4.	Forward voltage and fiber output power for the 40 devices measured at CERN

Figure 5.	Maximum value of the integral linearity deviation for the 40 devices measured at CERN

Figure 6 and Figure 7 show comparisons between CERN and ST measurements of Ith, Slope Efficiency and Forward Voltage. The scatter plots in Figure 6 show that there is a good correlation between ST and CERN measurements even if the measurements of the threshold performed at CERN are slightly bigger than the corresponding ST values. This could be due to difference in temperature at labs during measurements at ST and CERN. The difference is about 5% in average; CERN measurements are well inside the specifications, therefore we can accept the lasers.

Figure 6.	Comparison of CERN-measured Ith and efficiency with the ST measurements.

Figure 7.	Comparison of CERN-measured forward voltage with the ST measurements.

The spread in the distribution in Figure 7 shows that the CERN measurements of the forward voltage are well inside the specifications and even more stable, then corresponding ST values. Taking into account that the difference is not big (7.2% in average), lasers could be accepted.

### Dynamic Measurement

By applying a voltage pulse train to the laser under test it is possible to excite the laser to laser from below threshold. The resultant optical pulse observed on an oscilloscope with the aid of an optical probe allows to measure the relaxation oscillations of the laser die and thus determine the intrinsic bandwidth of the die without the sub-mount. A typical optical pulse is shown in Figure 8, while the extracted bandwidth and risetime are shown in Figure 9

Figure 8.	Optical output pulse as measured on an oscilloscope with optical probe. The laser bandwidth is determined from the relaxation oscillation frequency.

Figure 9.	Bandwidth and risetime for the 39 devices that were measured at CERN. All devices are in spec: Bandwidth>1GHz.

One device (ST ID XL416C56) did not pass dynamic test even after several measurements. Due to abnormal output pulse shape its bandwidth and risetime could not be calculated properly; therefore it is not shown in Figure 9.

# Conclusions

39 lasers out of 40 tested at CERN were found inside specification. At the same time, 1 device failed dynamic test, and 3 devices out of 80 did not pass visual inspection.

The decision is to accept the lot L24a.

# Footnotes

Laser Transmitter Quality Assurance Procedure, Version 1.2, 17 January 2003

CMS Tracker Optical Readout Link Specification, Part 2.2: Laser Transmitter, Version 3.5, 14 May 2002

# Text boxes

b

a

scratches

glue