Terminated Ruggedized Ribbon

Harness and Adapter

Lot acceptance Report

SUMITOMO ELECTRIC

5 January 2005

Batch B14c-B15c-B16c-B17c

Amendment 2

# Overview

In this document we report on the lot acceptance tests performed on 12 randomly sampled ruggedized ribbon harnesses terminated with sMU connectors by Sumitomo Electric, supplied also with 12-way sMU-MU adapters.  These 12 harnesses are from batches b14c, b15c, b16c and b17c. The sample origin is shown in Table 1.

| Batch | Delivery Date | Quantity | Length | Test Report | QA sample | End A QR code | End B QR code |
| --- | --- | --- | --- | --- | --- | --- | --- |
| B14c | Dec 2004 | 10 | 5.0m | 90-498-6014 | 1 | 0244 | 0261 |
|  |  | 10 | 6.0m | 90-498-6013 | 1 | 0232 | 0238 |
|  |  | 30 | 7.0m | 90-498-6012 | 1 | 0211 | 0267 |
| B15c | Dec2004 | 20 20 60 | 5.0m 6.0m 7.0m | 90-498-6011 90-498-6010 90-498-6009 | 1 1 1 | 0018 0009 0024 | 0173 0152 0100 |
| B16c | Jan 2005 | 10 10 30 | 5.0m 6.0m 7.0m | 90-498-6005 90-498-6004 90-498-6003 | 1 1 1 | 0324 0360 1757 | 1766 0398 1778 |
| B17c | Jan 2005 | 10 10 30 | 5.0m 6.0m 7.0m | 90-498-6008 90-498-6007 90-498-6006 | 1 1 1 | 1764 1716 1713 | 1767 1762 1724 |

Table 1: Sample origin (the QR code four digits are the last ones of the whole number: 3301306210####).

# Production Tests and Results

Testing was performed according to the procedures in CMS-TK-QP-0005, as summarized in Fig. 1 and Table 2.

Fig. 1: Acceptance flowchart.

Table 2:  Acceptance programme overview table.

| # | Specification to be tested | Test Specifications | CERN Testing |
| --- | --- | --- | --- |
|  |  | Min | Typ | Max | Units | Pre-production Qualification | Lot Acceptance |
| 3.1.1 | Number of channels | 12 |  | ( | ( |
| 3.1.2 | Operation Wavelength | 1310 | nm |  |  |
| 3.1.3 | Connector type | MU Simplified Plug |  | ( | ( |
| 3.1.4 | Number of mating cycles | 20 |  |  |  | ( |  |
| 3.1.5 | Random mate insertion loss |  |  | 0.6 | dB | ( | ( |
| 3.1.6 | Return loss | 45 |  |  | dB | ( | ( |
| 3.1.7 | Tensile loading on connector and furcation element |  |  | 10 | N |  |  |
| 3.1.8 | Harness length LH | 5, 6, 7 | m (+100mm –0mm) | ( | ( |
| 3.1.9 | Single fibre section length LF | 0.3 | m (+30mm –0mm) | ( | ( |
| 3.1.10 | Furcation element size | 25 x 10 x 5 | mm | ( | ( |
| 3.1.61 | Magnetic field |  |  | 4 | T |  |  |
| 3.1.62 | Hadronic fluence |  |  | 3×1014 | cm-2 |  |  |
| 3.1.63 | Gamma radiation dose |  |  | 1.5×105 | Gy(Si) |  |  |
| 3.1.64 | Temperature | -20 | -10 | 70 | °C |  |  |
| 3.1.65 | Operating humidity |  | Dry Nitrogen flow during operation. Dry lab environment during testing. |  |  |  |  |
| 3.1.81 | Material composition |  | Halogen-free, flame retardant material |  |  |  |  |

Legend:			( Visual Inspection	( Geometrical measurement	( Optical Test

## Visual Inspection

### Procedure

Visual inspection of all samples consisted of the following sequence:

- The sample was unpacked from its transportation container.

- It was carefully inspected for connector type, label position, colour and other macroscopic defects.

### Acceptance Criteria

- All samples shall be properly packaged.

- Labels shall be legible and properly attached to the connector.

- Connector type and colour should be as specified.

- All samples shall be free from visible defects.

### Results

- All samples were very well packaged.

- Labels were correctly attached.

- The connectors were as specified and the colour of the fibres was as specified.

Nevertheless we notice that for 3 harnesses 1 channel was clearly shorter than the others (~ 1.5cm). Because the length LF stay in specifications, these harnesses have no been rejected.

## Geometrical Measurement

### Procedure

The geometry was checked in the following way on all samples:

- The terminated harness length (LH) and the single-fibre lengths between the furcation element and adapter (LF) were measured. The definition of the length measurement is shown in Fig. 2.

2.  The length LH of all harnesses channels was measured with a high resolution OTDR. The length LF was measured with a ruler.

### Acceptance Criteria

The jumper length must be within the specified range for the particular overall length (Lnom –0mm/+100mm) and for the bare fibre length (Lnom –0mm/+30mm).  The nominal harness lengths were 5.0m, 6.0m, and 7.0m and the nominal individual fibre lengths was 0.30m.

Fig 2: Lengths definition. The length of the sMU plug does not

include the ceramic sleeve around the ferrule.

### Results

The geometrical measurements are shown in Table 3. Note that the 12 harnesses were arbitrarily numbered from 1 to 12.  Table 4 shows the OTDR results for each channel.  All the lengths were within the specified limits but because of 1 shorter channel, 3 lengths are closed to the specification 0.30 m.

Table 3: Measured lengths of harness samples.

| QR code sample | Harness arbitrary number | Length LF-A (Side A) (m) | Length LF-B (Side B) (m) |
| --- | --- | --- | --- |
| 0244/0261 | 1 | 0.304 | 0.315 |
| 0232/0238 | 2 | 0.315 | 0.315 |
| 0211/0267 | 3 | 0.315 | 0.313 |
| 0018/0173 | 4 | 0.312 | 0.310 |
| 0009/0152 | 5 | 0.315 | 0.313 |
| 0024/0100 | 6 | 0.314 | 0.314 |
| 0324/1766 | 7 | 0.300 | 0.310 |
| 0360/0398 | 8 | 0.312 | 0.312 |
| 1757/1778 | 9 | 0.313 | 0.300 |
| 1764/1762 | 10 | 0.300 | 0.310 |
| 1716/1762 | 11 | 0.310 | 0.310 |
| 1713/1724 | 12 | 0.310 | 0.310 |

(the QR code four digits are the last ones from the whole number: 3301306210####).

Table 4: OTDR measurement of all channels.

| Channel number | Length (m) n0 1 | Length (m) n0 2 | Length (m) n0 3 | Length (m) n0 4 | Length (m) n0 5 | Length (m) n0 6 | Length (m) n0 7 | Length (m) n0 8 | Length (m) n0 9 | Length (m) n0 10 | Length (m) n0 11 | Length (m) n0 12 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 01 | 5.065 | 6.061 | 7.029 | 5.046 | 6.057 | 7.048 | 5.066 | 6.052 | 7.061 | 5.058 | 6.055 | 7.054 |
| 02 | 5.064 | 6.057 | 7.066 | 5.046 | 6.061 | 7.048 | 5.066 | 6.059 | 7.056 | 5.049 | 6.055 | 7.053 |
| 03 | 5.059 | 6.042 | 7.054 | 5.045 | 6.058 | 7.063 | 5.064 | 6.066 | 7.064 | 5.041 | 6.053 | 7.061 |
| 04 | 5.061 | 6.021 | 7.052 | 5.047 | 6.058 | 7.054 | 5.063 | 6.059 | 7.062 | 5.047 | 6.052 | 7.050 |
| 05 | 5.065 | 6.054 | 7.044 | 5.063 | 6.060 | 7.064 | 5.068 | 6.065 | 7.064 | 5.064 | 6.053 | 7.064 |
| 06 | 5.058 | 6.070 | 7.058 | 5.059 | 6.064 | 7.063 | 5.069 | 6.062 | 7.058 | 5.042 | 6.054 | 7.061 |
| 07 | 5.053 | 6.064 | 7.078 | 5.045 | 6.080 | 7.063 | 5.070 | 6.060 | 7.066 | 5.034 | 6.057 | 7.063 |
| 08 | 5.059 | 6.065 | 7.031 | 5.054 | 6.058 | 7.048 | 5.063 | 6.061 | 7.066 | 5.046 | 6.058 | 7.057 |
| 09 | 5.061 | 6.053 | 7.057 | 5.045 | 6.069 | 7.074 | 5.058 | 6.066 | 7.064 | 5.049 | 6.055 | 7.065 |
| 10 | 5.059 | 6.050 | 7.059 | 5.060 | 6.057 | 7.077 | 5.051 | 6.062 | 7.065 | 5.045 | 6.056 | 7.065 |
| 11 | 5.049 | 6.069 | 7.061 | 5.049 | 6.065 | 7.058 | 5.067 | 6.062 | 7.065 | 5.066 | 6.057 | 7.065 |
| 12 | 5.057 | 6.062 | 7.044 | 5.046 | 6.071 | 7.065 | 5.067 | 6.063 | 7.057 | 5.061 | 6.054 | 7.047 |

## Optical Test A (during acceptance)

Optical properties were measured using the setup shown in Fig. 3. The harness was first measured connected in a given direction. If necessary, the measurement was repeated with the harness connected in the opposite sense (see 2.3.1).

Fig. 3: Measurement setup for insertion loss and return loss measurements

### Random mate insertion loss (all fibre channels).

The insertion loss (IL) is defined as the Log of the ratio of optical powers measured before (P0) and after (P1) insertion of the device under test.  The optical powers (P0 and P1) were measured with a large area detector in an optical head receptacle.

Insertion loss:

#### 2.3.1.a	Acceptance criteria

The acceptance criterion is such that the insertion loss shall be less than 0.6dB for one side.

Since both ends of the harness are effectively being measured at the same time using the setup shown in Fig. 3, it could be the case that the measured loss is greater than 0.6dB. If so, the harness is connected in the opposite sense and a second set of insertion loss measurements is performed.

In case the two measurements are above 0.6dB, the return lead is removed from the optical head (see Fig.3) and each connection with high insertion loss is measured individually.

#### 2.3.1.b	Results

The results are shown in Figures 4-5-6-7: all harnesses were found to be within specified limit.

Fig. 4: Insertion loss data b14c

Fig. 5: Insertion loss data b15c

Fig. 6: Insertion loss data b16c

Fig. 7: Insertion loss data b17c

The graphs in Figures 8-9-10-11 correlate Sumitomo manufacturing (MF) and CERN insertion loss values.

Fig. 8: b14c						      Fig. 9: b15c

Fig. 10: b16c							Fig.11:  b17c

### Return loss (all fibre channels).

The return loss (RL) is defined as the Log of the ratio of the reflected optical powers measured during referencing (Pref) and after (P1) insertion of the device under test (DUT).

Return loss: (1)

#### 2.3.2.a	Acceptance criteria

The acceptance criterion is such that the return loss shall be greater than 45dB.

#### 2.3.2.b	Results

The results are shown in Figure 12-13-14-15. All devices were well within the specified limit.

Fig. 12: Return loss data b14c.

Fig. 13 Return loss data b15c.

Fig. 14: Return loss data b16c.

Fig. 15: Return loss data b17c.

# Conclusions

The twelve12sMU-12sMU harnesses and adaptors supplied by Sumitomo Electric as batch b14c, b15c, b16c, b17c are in specification.  The individual fibre length will have to be more accurate because some of them are shorter of ~1.5cm which gives a length LF close to the specification of 0.30m. Nevertheless all the 250 harnesses for these batches are accepted.

# Footnotes

(1) Formula valid if using a reference with perfect glass-air interface.