Dense Multi-Ribbon Cable

Qualification

Sumitomo

Table of Contents

1	Overview	3

1.1	Qualification programme workflow	3

2	Technical qualification	4

2.1	Compliance with technical requirements	4

2.2	Qualification test results	6

2.2.1 Visual Inspection	6

2.2.2 Geometrical Measurement	6

2.2.3 Optical Measurement	7

2.3	Radiation Resistance	8

3	Conclusion	8

4	References	8

5	Appendix	9

5.1	Ericsson test data	9

# Overview

This report details the qualification tests made on one sample of multi-ribbon cable produced by Sumitomo.   Cable terminated with only 2 MPO connectors on each side (picture 1) was used to carry out the cable qualification.

This report summarizes the visual inspection, geometrical and optical tests performed on the cable.

Picture 1: picture of the multi-cable MPO terminated

## Qualification programme workflow

The qualification programme workflow is shown in Figure 1.  All test procedures for lot acceptance are described in document [3].  Tests are carried out at room temperature unless otherwise noted.  The geometrical tests are carried out with limited accuracy as they are intended to detect gross manufacturing defects only.

Figure 1:  Flow chart of qualification procedure.

# Technical qualification

## Compliance with technical requirements

Table 1 shows the specified performance of the cable against which the samples were tested and gives a summary of the results obtained in comparison with the specifications [4].

Table 1:  Specification test target taken from the technical specification.  Cells in gray indicate parameters not measured during qualification.

| # | Specification to be tested | Specification | CERN Qualification Results |
| --- | --- | --- | --- |
|  |  | Min | Typ | Max | Units | Measurement | Qualified? |
| Fibre |  |  |  |  |  |
| 4.1.1 | Fibre type | Single mode non-dispersion shifted |  |  |  |
| 4.1.2 | Fibre material | Phosphorus free |  |  |  |
| 4.1.3 | Geometry | 9/125/250 | m |  |  |
| 4.1.4 | Cladding diameter | 124 | 125 | 126 | m | ~125 | YES |
| 4.1.5 | Primary coating diameter |  | 250 |  | m | ~240 to ~250 | YES |
| 4.1.6 | Mode field concentricity error |  |  | 0.4 | m |  |  |
| 4.1.7 | Operation wavelength | 1260 | 1310 | 1330 | nm | 1310 | YES |
| 4.1.8 | Attenuation |  |  | 0.4 | dB/km |  |  |
| Ribbon |  |  |  |  |  |
| 4.1.21 | Number of channels | 12 |  | 12 | YES |
| 4.1.22 | Overall dimensions | 3100 x 320 | m | ~3150 x ~320 | YES |
| 4.1.23 | Pitch |  | 250 |  | m |  |  |
| 4.1.24 | Fibre to fibre skew |  |  | 10 | ps/m |  |  |
| 4.1.25 | Bend radius | 3 |  |  | cm |  |  |
| 4.1.26 | Torsion |  |  | 5 | turn/m |  |  |
| 4.1.27 | Tensile loadi\ng |  |  | 10 | N |  |  |
| 4.1.28 | Compressive strength |  |  | 3 | N/cm |  |  |
| 4.1.29 | Impact resistance |  |  | 2 | J |  |  |
| 4.1.30 | Fibre colour-code | Bellcore |  | Bellcore | YES |
| 4.1.31 | Ribbon colour | Transparent |  | Transparent | YES |
| 4.1.32 | Ribbon marking | Bar marking, repeated every 15cm |  | Bar every 20cm | YES |
| Cable |  |  |  |  |  |
| 4.1.41 | Number of channels | 96 |  | 96 | YES |
| 4.1.42 | Cable diameter |  | 8 | 10 | mm | 9.04 to 9.42 | YES |
| 4.1.43 | Bend radius | 8 |  |  | cm | 8 | YES |
| 4.1.44 | Torsion |  |  | 1 | turn/m | 1 | YES |
| 4.1.45 | Tensile loading |  |  | 500 | N |  |  |
| 4.1.46 | Compressive strength |  |  | 50 | N/cm |  |  |
| 4.1.47 | Impact resistance |  |  | 15 | J |  |  |
| 4.1.48 | Water resistance | Occasional radial immersion |  |  |  |
| 4.1.49 | Sheath colour | green |  |  | YES |
| 4.1.50 | Sheath marking | ERICSSON NETWORK TECHNOLOGIES year-week GAYGQBD 96x10/125 OPTICAL FIBRE SYSTEM HAZARD LEVEL 1 00000#m ------ |  | Text repeated every 1m. | YES |
| 4.1.51 | Cabe cut-off |  |  | 1260 | nm |  |  |
| 4.1.61 | Magnetic field |  |  | 4 | T |  |  |
| 4.1.62 | Hadronic fluence |  |  | 1×1012 | cm-2 | AVT3 | YES |
| 4.1.63 | Gamma radiation dose |  |  | 100 | Gy(Si) | AVT3 | YES |
| 4.1.64 | Temperature | -20 |  | 70 | °C |  |  |
| 4.1.65 | Operating humidity |  | 60 |  | %RH |  |  |
| 4.1.81 | Material composition |  | Halogen-free |  |  |  |  |
| 4.1.82 | Fire behaviour |  | IEC 332-3, 1034, 754-2, ABD0032 |  |  |  |  |

## Qualification test results

### Visual Inspection

- PASS: Cable correctly packaged in transport box.

- PASS: Ribbons undamaged inside cable sheath.

- PASS: Ribbon Colour coding correct.

- PASS: Ribbon marking on all ribbons.

- PASS: Cable colour gray.  Cable marking not on top of cable: BAD orientation.

### Geometrical Measurement

- PASS: Cable outer dimension: 9.04-9.42mm.  Ribbon dimension 3150x320µm.

- PASS: no residuals left on fibre after removal of ribbon matrix material.  Primary coating diameter 240-250µm.

- PASS: Cladding diameter is 125µm.

### Optical Measurement

Optical properties were measured by routing the 5m  cable section on a cube with 50cmx50cm facets, as shown in figure 2.  An insertion loss measurement was performed as the cable was bent 5 times on orthogonal facets.

Figure2:  Multi-ribbon cable routing on cube with 50cm long facets.

The target value for bending loss was not more than 0.1dB change.  The maximum change was measured to be –negligible. The Figure 3 shows the Insertion and return loss for each MPO connectors, male and female.

Figure3:insertion and return loss(dB)  for each MPO connectors .

## Radiation Resistance

The fibre used in the multi-ribbon cable was qualified by CERN as part of validation run AVT3 [1].  The cable radiation resistance was checked as part of the market-survey test campaign and is reported in Ericsson note OUP00.001 [2].

# Conclusion

- Cable passes acceptance criteria for geometrical and optical measurement.

- Bad ribbon orientation on the cable: need to be changed for production.

# References

[1]	Optical fibre advance validation test report AVT3, CMS-TK-TR-0029, CERN EDMS archive.

[2] 	Ericsson qualification test reports of Multi-Ribbon Cable, CMS-GE-TR-0015, CERN EDMS archive

[3] 	Dense Multi Ribbon Cable Quality Assurance Procedure, CMS-TK-QP-0007, CERN EDMS archive

[4] 	CMS Tracker Optical Readout Link Specification Part 4.1: Dense Multi-Ribbon Cable, CMS-GE-ES-0004, CERN EDMS archive

[5]	TP-04:499 Ericsson Report on Crush Test performed on pre-production batch c5, CMS-TK-TR-0039.

# Footnotes

Ericsson Specification reads “ERICSSON NETWORK TECHNOLOGIES year-week GAYGQBD 96x10/125 OPTICAL FIBRE SYSTEM HAZARD LEVEL 1 PxxxPyyyyyM -----” where x is the cable id and y the metre-marking.  This is the marking that appears on the cable.